## Slide 1: ECG Based Authentication
Handbook of Information and Communication Security, Springer 2010 (Book Chapter)
Authors – Fahim Sufi, Ibrahim Khalil, Jiankun Hu
Presented By –
Nafis Neehal (0415052110)
Dewan Ziaul Karim (0417052119)
Sejuti Banik (0417052004)
CSE 6811 – Wireless Ad Hoc Networks

## Slide 2: Electrocardiogram (ECG) Signals are now one of the emerging techniques for Biometric Authentication

## Slide 3: Biometric Systems and Inheritance of ECG
Biometric System – Template Matching
Acquired biometric data
Template Data
Several ways – DNA, Iris, Fingerprint, Retina, Voice etc.
DNA - One dimensional ultimate unique code for a person
ECG - Graphical record of the electrical impulses of the heart
ECG based biometric – A recent research topic

## Slide 4: Physiology of ECG
P wave
QRS complex
T wave
Inferior vena cava
Superior vena cava
Right atrium
Right ventricle
Left ventricle
Left atrium

## Slide 5: Feature Waves & Rhythm Analysis
Width
  A normal QRS complex 0.06–0.10 sec (Represented by 3 square boxes)
  PR interval - 120–200ms (3-5 boxes)
Amplitude
  Read in millivolt range
  Dependent on the sensitivity of ECG sensor
Direction and curvature
Feature set, F = Pm U (QRS)m U Tm , where ,
Pm = {P1, P2, P3, P4, P5},
(QRS)m = {(QRS)1 , (QRS)2 , (QRS)3 , (QRS)4 , (QRS)5 },
Tm = {T1, T2, T3, T4, T5}
RRu = time of occurrence(QRS)m − time of occurrence(QRS)m − 1
IHR =60/RR1, 60/RR2, 60/RR3, . . . ,60/Rru
HRV is the beat-to-beat alterations in heart rate

## Slide 6: ECG Biometrics Usage & Classification
Verification ECG (One to One matching)
PIN or name or smart card to identify himself and his acquired ECG is matched (one-to-one matching) with his own ECG template
Identification ECG (One to Many matching)
An individual’s biometric ECG is recorded and template matching is performed throughout the ECG template database.
ECG Biometrics Classification | 
Fiducial Point detection (Time Series Data) | ECG features extracted in the frequency domain

## Slide 7: Modern ECG Biometrics Classification
Direct Time Domain Feature Extraction
ECG Morphology (P duration, P amplitude, QRS duration, QRS amplitude, T duration, T amplitude, etc.)
Uniqueness of Beating Patterns (Patterns of consecutive hear beats. RR interval, IHR and HRV, breathing patterns)
ECG Morphology - Most primitive form of ECG features
Frequency Domain Feature Extraction
Wavelet Decomposition
Fourier Transform (stethoscope to obtain the Lubb–Dubb sound of heart)
Discrete Cosine Transform (DCT)

## Slide 8: Modern ECG Biometrics Classification
Neural Network
Template matching algorithms along with
Decision Based Neural Networks (DBNN)
Obtain 100% accuracy (experimented on 20 subjects)
Polynomial Based
Extract polynomial coefficients from ECG signal
Coefficients used as biometric templates
Statistical Approaches
Percentage Root-Mean-Square Difference (PRD)
Measure the quality of reconstructed ECG after lossy ECG compression
Cross Correlation (CC)
Technique used in statistics to match the similarity of signals
Least Discriminant Analysis (LDA), Autocorrelation and Mean–Variance of RR interval
Other Approaches for Feature Extraction

## Slide 9: Comparison of Existing ECG Biometric Systems
Higher Misclassification Rates - PRD, CC and WDM
Lower Misclassification Rates – PDM
Misclassification reasons –
Not prioritizing the ECG features
Occurrence of abnormal beats
Two algorithms solved these issues
FMR - Chances of a wrong person’s (different) enrolment data being matched against the recognition data provided
FNMR - Reflects the occurrences of the same person’s enrolment data and recognition data not being similar
Misclassifications and Accuracy
Misclassification rate for PRD,CC,WDM and proposed PDM
FRM and FNRR across different modalities

## Slide 10: Comparison of Existing ECG Biometric Systems
Template Size
Comparison of template sizes
Computational Cost
Comparison of number of operations (NOP)
for PRD, CC,WDM and PDM
Based on number of operations needed to compute
similarity matching between the enrolled data and
recognition data

## Slide 11: System Design of ECG Biometric
Enrolment: ECG template xu (5 heart beats) is enrolled into system
Verification:
After enrolment: a. System takes input of individual ECG yu b. Matches yu with xu using Sj (through PRD, CC and WDM) c. if result of function Sj is within threshold Γj, then A(I, yu) returns A1 else A(I, yu) returns A2
User Initiated: 1. User inputs identification data e.g. name, Pin etc. along with verification data yu 2. Corresponding ECG xu is fetched from template database 3. Finally Sj(xu, yu) performs necessary calculations as steps b and c of the after enrolment procedure.

## Slide 12: System Design of ECG Biometric
Identification:
Confidence Level, CL = 0.25X(100-PRD)+ 0.25X(100-CC)+ 0.5X(100-WDM)

## Slide 13: Difference Between Verification and Identification
The difference lies in the Decision Logic
B: PRD ≤ 14
C: CC ≥ 0.03
D: WDM ≤ 6
E: WDM ≥ 69.25
G: Person Recognized (Verified/Identified) .
Decision Logic for Verification | Decision Logic for Identification
G → B ∩ C ∩ D ∩ E | G → (D ∩ E) ∩ (B ∪ C)

## Slide 14: Software Implementation of ECG Biometric
Finding Threshold Γj:
2 ECGs each for 15 MIT-BIH people were acquired over a duration ( 1 week-month)
Matlab scripts for automating
For all cases PRD < 13.3 (<14), CC > 0.0351 (>.03) and WDM < 5.4 (<6)
Samples were also randomly cross checked for efficient threshold determination of threshold
Environment, Database and Dataset:
.net and MS Visual Studio 2005
SQL Server
Publicly available ECG data

## Slide 15: Software Implementation of ECG Biometric
Methodology:
“Identify Person” option matches sample with all templates in SQL server
The highest match (with highest CL value) fetched from the database
Name Picture and Recognition Data shown on the software screen.

## Slide 16: Open Issues of ECG Based Biometric System
Lack of Standardization of ECG Fiducial Points no exact location where the ECG feature wave boundaries lie minute variation in fiducial point position leads to misclassification in the substantial population domain
Time Variant Nature of ECG ECG tends to change under different physiological condition and time Solution: Body Sensor Network for synchronized heart rate monitoring
Pertinence of Random Abnormality in ECG Unable to work with ectopic or premature beats (abnormal and random)
Longer Duration for ECG Wave Acquisition Previous applications take upto 20s time to average 20 beats Not feasible for time critical systems
Longer Duration for ECGWave Acquisition size of ECG template 600B. But some algorithms take O(n2) with many features.
Lack of Experimental Data for Verification At least two sets of normal ECG data acquired over a moderate time interval is necessary. Available data were from hospital and even after ethical approval Very recently, ECG Wave Information provide large sets of ECG data

## Slide 17: Security Issues for ECG Based Biometric
ECG Encryption a. specialized permutation cipher (character shuffling) b. Key only to authorized personnel
ECG Anonymization a. Wavelet Decomposition to know Frequency and Time Domain b. Corrupting first one of wavelet coefficients
c. Combining all coefficients to recreate anonymized ECG
ECG Obfuscation
Fig: Part of Fully encoded ECG through mathematical Transformations

## Slide 18: Our Contribution
Previous ECG applications and Systems used 7-168 data Insufficient!
Our approach deals with 50,000 data and reduces the authentication time lag

## Slide 19: Identification Time Reduction in ECG Based Authentication using K-Means Clustering for Biometric Templates

## Slide 20: Objective
Reduce Identification time in ECG based authentication (one to many matching)
Ensure highest possible accuracy
Ensure zero tolerance for False Positives (FMR Value / FAR) and lower rate of False Negatives (FNMR value / FRR)
Achieve optimal number of clusters

## Slide 21: Literature Review [1]
ECG Compression for time reduction in Identification
They have used one-person-one-cluster technique and used multiple entries for one person and considered all the entries of one person as a single cluster. So if there are n persons, there would be n clusters which definitely would not be that much of a time reduction
Used 16 Features for each entry identification after applying dimensionality reduction from initial 157 features. Although they have achieved 100% misclassification rate, but that is in terms of FNMR, they haven’t said anything about FMR values
They have converted ECG to a compressed characterized form. The compression procedure itself would consume a significant amount of time each and every time a user wants to authenticate, but they haven’t considered it in time of performance measurement
They haven’t shown any clear run-time comparison data with other existing ECG Based Authentication methods
Nothing on optimal cluster selection (as they are considering each person’s data as one cluster)

## Slide 22: Literature Review [2]
Fiducial feature reduction analysis for ECG based authentication
Applied only PCA, LDA, IGR etc. which can lead to reduction in dimension.
They haven’t done anything on clustering which might have lead to a data partition and reduction in number of entries to search

## Slide 23: Proposed Methodology
ECG Signal Acquire
Fiducial Features Extraction
Optimal Cluster Number Selection (Time Reduction, Accuracy, Elbow, Silhouette Score)
Data Preprocessing (Cleaning, Extrapolate, Scale)
Automated Physical Data Partition (Initial Batch Enrollment) according to Cluster Values
Predict Test Data Cluster
Search only values in the predicted cluster
Repeat, Until Convergence with fulfilled Objective Maximization

## Slide 24: Dataset (ECG-ViEW II)
ECG-ViEW II database was used
9 Fiducial Features, namely – RR interval, PR Interval, QRS Duration, QT Interval, QTc Interval, P Axis, QRS Axis, T Axis and age-adjusted Charlson comorbidity index (ACCI) Value
Worked on Partial Data with around 50k entries
Yet to work on the full ECG-ViEW II dataset consisting of around 1 Million ECG record

## Slide 25: Data Preprocessing
After data was acquired, the missing values were filled with zeros.
For the users having multiple ECG enrolled, the mean of there enrollment values were taken and other multiple enrollment data were removed.
Data was rounded to the nearest integer value
Finally data was scaled and transformed using StandardScaler() – remove mean and scale to unit variance
After this stage, we had around total 23k entries

## Slide 26: Data Clustering
ALGORITHM (dataset): return partitionedDataset
                cluster_range := [2, 10]
                FOR each_cluster in cluster_range:
                centroids = each_cluster.Centroids_
                FOR each_entry in dataset:
                min_cluster_label = min(Eudistance(each_entry, ))
      assign (each_entry, min_cluster_label)
      sort (dataset, cluster_label, ASC = 1)
      create_physical_partition_according_to_cluster_label()
      RETURN partitioned_files()

## Slide 27: Data Identification time Reduction
ALGORITHM (partitionedDataset, Dataset, testData, K): return timeReduction
                filesPartitioned = K
                FOR each_entry in testData:
                min_cluster_label = min(Eudistance(each_entry, ))
                timer1.start()
                access_clusterDataFile(partitionedDataset)
                min_id_c = min(Eudistance(each_entry, ))
                timer1.stop()
                timer2.start()
                access_serialDataFile(Dataset)
                min_id_s = min(Eudistance(each_entry, ))
                timer2.stop()
                RETURN (abs(timer2.time() – timer1.time()) / timer2.time())*100

## Slide 28: Performance Evaluation

## Slide 29: Optimal K Selection (Elbow Method)

## Slide 30: Optimal K Selection (Silhouette Score, K = 2)
Average Silhouette Score of Cluster – 0.3948

## Slide 31: Optimal K Selection (Silhouette Score, K = 3)
Average Silhouette Score of Cluster – 0.3160

## Slide 32: Optimal K Selection (Silhouette Score, K = 4)
Average Silhouette Score of Cluster – 0.3551

## Slide 33: Optimal K Selection (Silhouette Score, K = 5)
Average Silhouette Score of Cluster – 0.3240

## Slide 34: Optimal K Selection (Silhouette Score, K = 6)
Average Silhouette Score of Cluster – 0.2820

## Slide 35: Optimal K Selection (Silhouette Score, K = 7)
Average Silhouette Score of Cluster – 0.2917

## Slide 36: Optimal K Selection (Silhouette Score, K = 8)
Average Silhouette Score of Cluster – 0.2793

## Slide 37: Optimal K Selection (Silhouette Score, K = 9)
Average Silhouette Score of Cluster – 0.2451

## Slide 38: Optimal K Selection (Silhouette Score, K = 10)
Average Silhouette Score of Cluster – 0.2478

## Slide 39: Optimal K Selection (Silhouette Score VS Cluster)

## Slide 40: Cluster Comparison K vs (Time Reduction, Accuracy))

## Slide 41: Final Decision
Based on, Elbow Method and Silhouette score, K = 5 is giving the most optimal clustering (elbow bent is starting from there).
In terms of time reduction, K = 9 is performing best (74.38%). But, it’s silhouette score is lowest. So ultimately what is happening is, if we keep reducing cluster size, obviously time reduction will be higher too. But, we cannot also lose the cluster quality and accuracy.
In terms of accuracy, K = 3, 5 is giving 100% accuracy
We have to choose (simple decision logic) –
  [ = timeReduction, = accuracy, = silhouetteScore ]

## Slide 42: Final Decision
K | (Time Reduction) | (20%) | (Accuracy) | (50%) | (Silhouette Score) | (30%) | 
2 | 18.57 | 0.2 | 97 | 0.5 | 0.39 | 0.3 | 52.331
3 | 57.37 | 0.2 | 100 | 0.5 | 0.32 | 0.3 | 61.57
4 | 73.10 | 0.2 | 96 | 0.5 | 0.35 | 0.3 | 62.725
5 | 79.26 | 0.2 | 100 | 0.5 | 0.32 | 0.3 | 65.95
6 | 80.95 | 0.2 | 94 | 0.5 | 0.28 | 0.3 | 63.27
7 | 83.43 | 0.2 | 98 | 0.5 | 0.29 | 0.3 | 65.77
8 | 82.34 | 0.2 | 98 | 0.5 | 0.27 | 0.3 | 65.54
9 | 86.14 | 0.2 | 97 | 0.5 | 0.24 | 0.3 | 65.8
K |  |  |  |  |  |  | 
2 | 18.57 | 0.2 | 97 | 0.5 | 0.39 | 0.3 | 52.331
3 | 57.37 | 0.2 | 100 | 0.5 | 0.32 | 0.3 | 61.57
4 | 73.10 | 0.2 | 96 | 0.5 | 0.35 | 0.3 | 62.725
5 | 79.26 | 0.2 | 100 | 0.5 | 0.32 | 0.3 | 65.95
6 | 80.95 | 0.2 | 94 | 0.5 | 0.28 | 0.3 | 63.27
7 | 83.43 | 0.2 | 98 | 0.5 | 0.29 | 0.3 | 65.77
8 | 82.34 | 0.2 | 98 | 0.5 | 0.27 | 0.3 | 65.54
9 | 86.14 | 0.2 | 97 | 0.5 | 0.24 | 0.3 | 65.8
Choose K = 5 for this Dataset

## Slide 43: Final Remarks and yet to include in this project
Our preliminary analysis shows promising results in case of time reduction (79.26%)
Run full simulation on the 1 Million ECG ViEW Dataset and get more analysis (Problematic due to lack of proper hardware - GPU)
Also we need to find out FAR / FRR ratio as another performance metric.

## Slide 44: Future Work
Apply PCA for dimensionality reduction which will reduce more time as template size will degrade

## Slide 45: References
Faster person identification using compressed ECG in time critical wireless telecardiology applications, Sufi et. al. , Journal of Network and Computer Applications, Volume 34, Issue 1, January 2011, Pages 282-293
Fiducial feature reduction analysis for electrocardiogram (ECG) based biometric recognition, Tantawi et. Al. , Journal of Intelligent Information Systems, Volume 40, Issue 1, Pages 17-39

## Slide 46: Thank You